## Slide 1
Locating Faulty Rolling Element Bearing Signal by Simulated Annealing
Jing Tian
Course Advisor: Dr. Balan, Dr. Ide
Research Advisor: Dr. Morillo
AMSC 663 Mid Year Presentation, Fall 2012

## Slide 2: Background
Rolling element bearings are used in rotating machines in different industry sections.
Wind turbine gearbox
Computer cooling fan
Bearings
Bearings inside
Gas turbine engine
Induction motor
Bearing
Bearing
http://en.wikipedia.org/wiki/File:J85_ge_17a_turbojet_engine.jpg
http://en.wikipedia.org/wiki/File:Silniki_by_Zureks.jpg
http://en.wikipedia.org/wiki/File:Scout_moor_gearbox,_rotor_shaft_and_brake_assembly.jpg

## Slide 3: Health Monitoring of Bearing
Bearing failure is a concern is a concern for many industrial sections
  Bearing fault is a main source of system failure, e.g.: Gearbox bearing failure is the top contributor of the wind turbine’s downtime [1, 2].
  The failure of bearing can result in critical lost, e.g.: Polish Airlines Flight 5055 Il-62M crashed because of bearing failure [3].
Vibration signal is widely used in the health monitoring of bearing
  It is sensitive to the bearing fault. The fault can be detected at an early stage.
  It can be monitored in-situ.
  It is inexpensive to acquire.
Offshore wind turbines
http://en.wikipedia.org/wiki/File:DanishWindTurbines.jpg
http://en.wikipedia.org/wiki/File:LOT_Ilyushin_Il-62M_Rees.jpg
LOT Polish Airlines Il-62M

## Slide 4: Project Objectives
How to detect the bearing fault? Test if the vibration signal x(t) contains the faulty bearing signal s(t)
  Faulty bearing: x(t) = s(t) + ν(t)
  Normal bearing: x(t) = ν(t), where v(t) is the noise, which is unknown
How to test the existence of faulty bearing signal s(t)? Check if unique frequency component of s(t) can be extracted.
  Faulty bearing signal is a modulated signal : s(t) = d(t)c(t)
  d(t) is the modulating signal. Its frequency component is the fault signature. The frequency is provided by the bearing manufacturer.
  c(t) is the carrier signal, which is unknown.
Objective of the project: given vibration signal x(t), test if the frequency component of d(t) can be extracted.

## Slide 5: Approach
Use FIR filter-bank to decompose the test signal into sub-signals.
Use spectral kurtosis (SK) to locate the sub-signal which contains faulty bearing signal s(t). SK is the kurtosis of the discrete Fourier transform of the vibration signal. The sub-signal containing faulty bearing signal has higher SK [4].
Apply simulated annealing (SA) to optimize the frequency band of the located sub-signal.
  The optimum frequency band is determined by the optimum filter.
  The filter is optimized by solving the following problem:
Perform envelope analysis (EA) to the sub-signal which has the optimum frequency band to extract the fault feature frequency (modulating frequency)
fc is the frequency band’s central frequency; Δf is the width of the band; M is the order of FIR filter; fFaul is the fault feature frequency; fs is the sampling rate.

## Slide 6: Flow Chart of the Algorithm
FIR filter
hi (fci, Δfi, Mi)
SK
SA
Maximize SK by fc, Δf, M
Optimized FIR filter
h(fco, Δfo, Mo)
EA
x(n)
yi(n)
SKi
x(n)
yo(n)
FFT
a(n)
Magnitude
A(f)
|A(f)|
Maximized SK
SKo
f=fFault?
The bearing is faulty
The bearing is normal
Yes
No
x(n) is the sampled vibration signal;
yi(n) is filtered output of the ith FIR filter hi;
SKi is the SK of the yi(n);
yo(n) is the output of the optimized FIR filter;
a(n) is the envelope of yo(n) ;
A(f) is the FFT of a(n)

## Slide 7: Filter-bank

## Slide 8: Band-Pass Filter the Vibration Signal
Matlab’s built-in function “fir1” is used. It uses the following method
hd(n) is the impulse response of the filter
w(n) is the Hamming window
Therefore, the filtered signal y(n) is a function of fc, Δf, M.
M is the order of the filter. bi is the coefficient of the filter.
FIR filter is defined as

## Slide 9
Initial Input for Simulated Annealing
Initial input w(fc1, Δf1, M1) is obtained by calculating SK for a binary tree of FIR filter-bank.
  Output of the jth filter at level k is
  Structure of the filter-bank
Frequency bands are ranked according to their SK value from large to small. Top h frequency bands are selected as the initial input.

## Slide 10: Validation of the Filter-bank
The test signal has four frequency components.
  One component locates at the edge of two filters in frequency domain.
  Two components locates near the edge of the filter.

## Slide 11: Validation of the Filter-bank
  Two level filter-bank is used, which has 4 filters. For sampling rate = 1024Hz, the filters are [0, 128]Hz, [128, 256]Hz, [256,384]Hz, [384, 512]Hz
  Frequency components are observed in the right frequency bands. But the magnitude is reduced.
Magnitude=9.5
Magnitude=7.6
Magnitude=2.85
Magnitude=2.85, 3.8

## Slide 12: Spectral Kurtosis

## Slide 13: Spectral Kurtosis
Definition of spectral kurtosis
Estimation of spectral kurtosis
  DFT of a stationary signal is a circular complex random variable, and E[Y(m)2]=0, E[Y* (m)2]=0. [5]
where Y(m) is the DFT of the signal y(n); κr is the rth order cumulant. Both y(n) and Y(m) are N points sequences. SK is a real number.

## Slide 14: Result of SK
The SK have small value for white noise and high values for periodic signal.
  White noise, SK = -0.0406
  Pure periodic signal , SK = 510

## Slide 15: Simulated Annealing

## Slide 16
Simulated annealing [6] is a metaheuristic global optimization tool.
In each round of searching, there is a chance that worse result is accepted. This chance drops when the iterations increase. By doing so, the searching can avoid being trapped in a local extremum.
Initialize the temperature T
End a round of searching
Use the initial input vector W
Compute function value SK(W)
Generate a random step S
Compute function value SK(W+S)
SK(W+S) < SK(W)
exp[(SK(W) - SK(W+S) )/T] > rand ?
Termination criteria reached?
Replace W with W+S, reduce T
Keep x unchanged, reduce T
Yes
No
Yes
Yes
No
Simulated Annealing

## Slide 17: Validation of SA: 1-D Function
One dimensional function optimization
  The function has a global minimum and many local minimums.
  The function is used to check the fundamental of the algorithm.
  The global minimum is y=-100 when x= π

## Slide 18
Initialize the temperature T
End a round of searching
Use the initial input vector W
Compute function value SK(W)
Generate a random step S
Compute function value SK(W+S)
SK(W+S) < SK(W)
exp[(SK(W) - SK(W+S) )/T] > rand ?
Termination criteria reached?
Replace W with W+S, reduce T
Keep x unchanged, reduce T
Yes
No
Yes
Yes
No
Setting of the SA
T = 1000
W: A random number in [-10,10]
S: A random number in [-10,10]
T = 0.99T
T = 0.99T
1,000 iterations

## Slide 19: Validation of SA: Result
Result
  SA ends at 1,000 iterations. The optimum is found at 943th iteration.
  The minimum found is -99.9996,
  Optimum variable x= 3.1389

## Slide 20
Three dimensional function optimization
  The function has three variables, it is used to validate the algorithm…
  The global minimum is y=-150 when x1= π, x2=0, and x3=- π.
Validation of SA: 3-D Function

## Slide 21
Initialize the temperature T
End a round of searching
Use the initial input vector W
Compute function value SK(W)
Generate a random step S
Compute function value SK(W+S)
SK(W+S) < SK(W)
exp[(SK(W) - SK(W+S) )/T] > rand ?
Termination criteria reached?
Replace W with W+S, reduce T
Keep x unchanged, reduce T
Yes
No
Yes
Yes
No
Setting of the SA
T = 1000
W: A vector, each element is a number in [-10,10]
S: A vector, each element is a number in [-10,10]
T = 0.99T
T = 0.99T
100,000 iterations

## Slide 22
Validation of SA: Setting and Result
Result
  SA ends at 100,000 iterations. The optimum is found at 76,455th iteration.
  The minimum found is -149.5179
  Optimum variable x= [3.1437 15.6941 -12.5659]

## Slide 23: Envelope Analysis

## Slide 24
The enveloped signal is obtained from the magnitude of the analytic signal.
The analytic signal is constructed via Hilbert transform.
Hilbert transform shifts the signal by π/2 via the following formula
The analytic signal is constructed
Magnitude of the analytic signal forms the enveloped signal.
Original signal
Hilbert transform of the original signal
Enveloped signal
Envelope Analysis

## Slide 25
A modulated signal y is used to validate the algorithm.
Validation of Envelope Analysis: Test Signal
200Hz
190Hz
210Hz

## Slide 26
After envelope analysis, modulating signal is obtained with a different magnitude.
After FFT, the modulating frequency component is obtained.
Validation of Envelope Analysis
10Hz

## Slide 27: Progress
October
  Literature review; exact validation methods; code writing
November
  Middle: code writing
  End: Validation for envelope analysis and spectral kurtosis
December
  Semester project report and presentation
February
  Complete validation
March
  Adapt the code for parallel computing
April
  Validate the parallel version
May
  Final report and presentation

## Slide 28: Remaining Work at this Stage
Complete the validation of spectral kurtosis.
Put the sub-programs together to a single program.
Validate the whole program.

## Slide 29: References
[1] Wind Stats Newsletter, 2003–2009, vol. 16, no. 1 to vol. 22, no. 4, Haymarket Business Media, London, UK
[2] H. Link; W. LaCava, J. van Dam, B. McNiff, S. Sheng, R. Wallen, M. McDade, S. Lambert, S. Butterfield, and F. Oyague,“Gearbox Reliability Collaborative Project Report: Findings from Phase 1 and Phase 2 Testing", NREL Report No. TP-5000-51885, 2011
[3] Plane crash information
http://www.planecrashinfo.com/1987/1987-26.htm
[4] J. Antoni, “The spectral kurtosis: a useful tool for characterising non-stationary signals”, Mechanical Systems and Signal Processing, 20, pp.282-307, 2006
[5] P. O. Amblard, M. Gaeta, J. L. Lacoume, “Statistics for complex variables and signals - Part I: Variables”, Signal Processing 53, pp. 1-13, 1996
[6] S. Kirkpatrick, C. D. Gelatt, and M. P. Vecchi, "Optimization by Simulated Annealing". Science 220 (4598), pp. 671–680, 1983