## Slide 1
Locating Faulty Rolling Element Bearing Signal by Simulated Annealing
Jing Tian
Course Advisor: Dr. Balan, Dr. Ide
Research Advisor: Dr. Morillo,
AMSC 663 Project Proposal, Fall 2012

## Slide 2: Background
Bearing provides relative rotational freedom and transmits a load between two structures.
Inner Ring
Cage
Rolling Elements
Outer Ring
Wind Turbine Gearbox
Construction of a bearing
http://en.wikipedia.org/wiki/Rolling_element_bearing
http://en.wikipedia.org/wiki/File:J85_ge_17a_turbojet_engine.jpg
Bearings
Bearings inside
Gas Turbine Engine
Induction Motor
Bearing
http://en.wikipedia.org/wiki/File:Silniki_by_Zureks.jpg
http://en.wikipedia.org/wiki/File:Scout_moor_gearbox,_rotor_shaft_and_brake_assembly.jpg

## Slide 3: Failure of Bearing
Bearing is a main source of system failure
  Motor bearing faults account for more than 40% of the induction motor’s failure [1].
  Gearbox bearing failure is the top contributor of the wind turbine’s downtime [2, 3].
Bearing is cheap, but the failure of bearing is costly.
  A $5,000 wind turbine bearing replacement can easily turn into a $250,000 project, not to mention the cost of downtime [4]
  In 1987, LOT Polish Airlines Flight 5055 Il-62M crashed because of failed bearings in one engine, killing all the183 people on the plane [5].
Offshore wind turbines
http://en.wikipedia.org/wiki/File:DanishWindTurbines.jpg
http://en.wikipedia.org/wiki/File:LOT_Ilyushin_Il-62M_Rees.jpg
LOT Polish Airlines Il-62M

## Slide 4: Health Monitoring of Bearing
Early detection of the bearing fault is a major concern for the industry.
  Incipient bearing fault is difficult to be detected.
  When a bearing has an incipient fault, it may still be operable for sometime. If the fault can be detected, maintenance can be scheduled.
Vibration acceleration signal is widely used in the fault detection of the bearing because
  It is sensitive to the bearing fault
  It can be monitored in-situ

## Slide 5: Bearing Fault Detection
The objective of bearing fault detection is to test if the vibration signal x(t) contains the faulty bearing signal s(t)
  Faulty bearing: x(t) = s(t) + ν(t)
  Normal bearing: x(t) = ν(t), where v(t) is the noise, which is unknown
Faulty bearing signal is a modulated signal [6]: s(t) = d(t)c(t)
  d(t) is the modulating signal. Its frequency component is the fault signature. The frequency is provided by the bearing manufacturer.
  c(t) is the carrier signal, which is unknown.
  The detection becomes to test if the fault signature can be extracted from x(t).
1/fFault
fFault is the fault signature

## Slide 6: Challenge
A popular method to extract the modulating frequency is envelope analysis.
  Problem: In the presence of noise the extraction may fail.
The solution is to band-pass filter the vibration signal in the frequency domain:
  Keep the faulty bearing signal
  Remove or reduce the noise components near it.
Challenge: how to find the optimum frequency band for the faulty bearing signal?
Faulty bearing signal

## Slide 7: Approach
Candidate frequency bands for the faulty bearing signal are examined by spectral kurtosis (SK)
  The frequency band for the faulty bearing signal has larger SK [7].
The optimum frequency band is found by simulated annealing (SA).
  The optimum frequency band is determined by the optimum filter.
  The filter is optimized by solving the following problem:
Envelope analysis (EA) is applied to the optimum frequency band to extract the fault feature frequency (modulating frequency)
fc is the frequency band’s central frequency; Δf is the width of the band; M is the order of FIR filter; fFaul is the fault feature frequency; fs is the sampling rate.

## Slide 8: Flow Chart of the Algorithm
FIR filter
hi (fci, Δfi, Mi)
SK
SA
Maximize SK by fc, Δf, M
Optimized FIR filter
h(fco, Δfo, Mo)
EA
x(n)
yi(n)
SKi
x(n)
yo(n)
FFT
a(n)
Magnitude
A(f)
|A(f)|
Maximized SK
SKo
f=fFault?
The bearing is faulty
The bearing is normal
Yes
No
x(n) is the sampled vibration signal;
yi(n) is filtered output of the ith FIR filter hi;
SKi is the SK of the yi(n);
yo(n) is the output of the optimized FIR filter;
a(n) is the envelope of yo(n) ;
A(f) is the FFT of a(n)

## Slide 9: Band-Pass Filter the Vibration Signal
The vibration signal x(n) is band-pass filtered by an FIR filter designed with window method.
hd(n) is the impulse response of the filter
w(n) is the Hamming window
Therefore, the filtered signal y(n) is a function of fc, Δf, M.

## Slide 10: Spectral Kurtosis
Definition of spectral kurtosis
Estimation of spectral kurtosis
  DFT of a stationary signal is a circular complex random variable, and E[Y(m)2]=0, E[Y* (m)2]=0. [8]
where Y(m) is the DFT of the signal y(n); κr is the rth order cumulant. Both y(n) and Y(m) are N points sequences. SK is a real number.

## Slide 11: Transmission of the Variables
fc, Δf, M become variables of SK in the following route.
Filter
DFT
SK

## Slide 12
Initial Input for Simulated Annealing
Initial input w(fc1, Δf1, M1) is obtained by calculating SK for a binary tree of FIR filter-bank.
  Output of the jth filter at level k is
  Structure of the filter-bank
Frequency bands are ranked according to their SK value from large to small. Top h frequency bands are selected as the initial input.

## Slide 13
Simulated annealing [9] is a metaheuristic global optimization tool.
In each round of searching, there is a chance that worse result is accepted. This chance drops when the iterations increase. By doing so, the searching can avoid being trapped in a local extremum.
Several rounds of searching are performed to find the global optimum.
Initialize the temperature T
End a round of searching
Use the initial input vector W
Compute function value SK(W)
Generate a random step S
Compute function value SK(W+S)
SK(W+S) > SK(W)
exp[(SK(W) < SK(W+S) )/T] > rand ?
Termination criteria reached?
Replace W with W+S, reduce T
Keep x unchanged, reduce T
Yes
No
Yes
Yes
No
Maximize SK by Simulated Annealing

## Slide 14
The enveloped signal is obtained from the magnitude of the analytic signal.
The analytic signal is constructed via Hilbert transform.
Hilbert transform shifts the signal by π/2 via the following formula
The analytic signal is constructed
Magnitude of the analytic signal forms the enveloped signal.
Original signal
Hilbert transform of the original signal
Enveloped signal
Envelope Analysis

## Slide 15: Implementation
Hardware
  The program will be developed and implemented on a personal computer.
Software
  The program will be developed with Matlab.
Parallel computing
  Simulated annealing has independent loops. Parallel computing will be implemented on this module.
  Parallel computing version programs will be developed with Matlab parallel computing tool box.

## Slide 16: Database
Database of this project was published by the Bearing Data Center of Case Western Reserve University [10].
It has four groups of data
  One group of normal baseline data.
  Three groups of bearing fault data.
  Each group of data has vectors corresponding to different motor loads and bearing fault conditions.
Artificial noise will be added to the data.
  Additive Gaussian white noise
  Discrete frequency noise
Normal bearing data
Faulty bearing data

## Slide 17: Validation
Validation includes module validation and the overall validation
Module validation
Overall validation
Validation | Input | Control Result | Test Result
SK | A simplified signal | Analytic solution | Numerical solution
Filter-bank | A signal with multiple frequency components | Pre-determined frequency components | Numerical solution
SA | A 3-parameter function | Pre-determined maximum | Numerical solution
EA | A modulated signal | Pre-determined modulating frequency | Numerical solution
Validation | Input | Control Result | Test Result
Overall | Real bearing signal | Pre-determined fault feature frequency | Numerical solution

## Slide 18: Deliverables
Matlab code
Test result
Final report
Final presentation
Database

## Slide 19: Schedule
October
  Literature review; exact validation methods; code writing
November
  Middle: code writing
  End: Validation for envelope analysis and spectral kurtosis
December
  Semester project report and presentation
February
  Complete validation
March
  Adapt the code for parallel computing
April
  Validate the parallel version
May
  Final report and presentation

## Slide 20: References
[1] L. M. Popa, B.-B. Jensen, E. Ritchie, and I. Boldea, “Condition monitoring of wind generators,” in Proc. IAS Annu. Meeting, vol. 3, 2003, pp. 1839-1846.
[2] Wind Stats Newsletter, 2003–2009, vol. 16, no. 1 to vol. 22, no. 4, Haymarket Business Media, London, UK
[3] H. Link; W. LaCava, J. van Dam, B. McNiff, S. Sheng, R. Wallen, M. McDade, S. Lambert, S. Butterfield, and F. Oyague,“Gearbox Reliability Collaborative Project Report: Findings from Phase 1 and Phase 2 Testing", NREL Report No. TP-5000-51885, 2011
[4] C. Hatch, “Improved wind turbine condition monitoring using acceleration enveloping,” Orbit, pp. 58-61, 2004.
[5] Plane crash information
http://www.planecrashinfo.com/1987/1987-26.htm
[6] P. D. Mcfadden, and J. D. Smith, “Model for the vibration produced by a single
point defect in a rolling element bearing,” Journal of Sound and Vibration, vol. 96,
pp. 69-82, 1984.

## Slide 21: References
[7] J. Antoni, “The spectral kurtosis: a useful tool for characterising non-stationary signals”, Mechanical Systems and Signal Processing, 20, pp.282-307, 2006
[8] P. O. Amblard, M. Gaeta, J. L. Lacoume, “Statistics for complex variables and signals - Part I: Variables”, Signal Processing 53, pp. 1-13, 1996
[9] S. Kirkpatrick, C. D. Gelatt, and M. P. Vecchi, "Optimization by Simulated Annealing". Science 220 (4598), pp. 671–680, 1983
[10] Case Western Reserve University Bearing Data Center
http://csegroups.case.edu/bearingdatacenter/home