## Slide 1
Design of Ant-Inspired Stochastic Control Strategies for Boundary Coverage and Collective Transport by Robotic Swarms
Contribution
Simulation and Results
Future Work
A bio-inspired, leaderless, decentralized boundary coverage and cooperative manipulation control scheme is developed for a robotic swarm. This control scheme is validated by mimicking an observed and modeled group transport behavior exhibited by Novomessor cockerelli (Kumar et al. HSCC 2013).
Individual Robot Controller
State-transition diagram of robot controller for collective transport. The diagram outlines a program that would run on a single robot. Here, puS and pbS are designed probabilities to unbind (detach) and bind (attach) respectively to side S.
While attached, robots lift the load to alleviate friction. Robots attached to the front pull with a force according to a proportional velocity controller.
Autonomous Collective Systems Laboratory ACS Lab
http://faculty.engineering.asu.edu/acs/
Approach
Attached to Back
Attached to Front
Load
Use a macroscopic population dynamic model to design enzyme-inspired stochastic control policies that allocate a robotic swarm around multiple boundaries. This model is used to synthesize three sets of stochastic robot attachment-detachment policies for tasks where a robot swarm must achieve non-uniform spatial distributions around multiple loads and transport them at a constant velocity.
Chemical Reaction Network Model
The notation r + US represents the event of a free robot (r) encountering an unbound zone on the side S (US), where S ϵ {Front (F), Back (B)}.
The notation represents how often such encounter events occur and result in the free robot (r) binding to the unbound zone (US) to produce a new bound zone .
Methods
Simplified Load Dynamics
(1)
(2)
Sean Wilson et al. Design of Ant-Inspired Stochastic Control Policies for Collective Transport by Robotic Swarms. Swarm Intelligence, 8(4):303-327, Dec. 2014.
Controller Synthesis
Equilibrium Population Matching Method (EPMM) : Only requires the encounter rate ratio () to design the probabilities of attaching and detaching (pbS, puS ) through Eq. 1. This allows for the fastest convergence time to the equilibrium population states but ignores the transient population dynamics.
Transient Matching Method (TMM) : Requires the absolute encounter rates (, ) from Eqs. 1 and 2 to design the probabilities of attaching and detaching (pbS, puS ) through Eq. 1. This design converges slower than the EPMM but matches the population transient rise time.
Rate Matching Method (RMM) : Requires the absolute encounter rates (, ) from Eqs. 1 and 2 to design the probabilities of attaching and detaching (pbS, puS ). The design equates the rates in two Markov Chain descriptions of the macroscopic model. This design matches fluxes into and out of states but does not allow for matching of equilibrium populations.
Validate results on the Pheeno robotic platform.
Expand analysis to dynamic boundaries.
Investigate methods to “turn off” the attachment-detachment process.
100 simulations are run for each control design (EPMM, TMM, RMM). For each run, 200 1-cm radius unattached robots, with parameters from the ant experiments, are initialized randomly in a 125 cm x 50 cm environment. A rigid circular load with radius 8 cm and mass 2.3 g is placed in the arena with the robots.
Estimating Encounter Rates
Director: Dr. Spring Berman